## Slide 1: STATUS OF SPOT VEGETATION
VEGETATION 2
NEW STANDARD PRODUCTS
VEGETATION 2002
Gilbert Saint - VEGETATION Programme Scientist

## Slide 2: VEGETATION 2
Same instrument as VEGETATION 1 with minor improvements on optics (less stray light, better detector homogeneity...) and to increase life time to 5 years
SPOT 5 having a star tracker, should provide better geometry without Ground Control Points (VGT 1 : 0.1 multispectral, 0.3 multitemporal for >90% pixels)
Ready for launch, waiting for availability of launch pad : last known date is May 3rd
Commissionning phase should last 2 month, after which the two instruments will be available, VGT 2 as the principal one, VGT 1 to complement for special acquisitions.

## Slide 3: NEW STANDARD PRODUCTS
From the beginning, Image Processing Center designed to accomodate for regular improvements of standard processing methods. New methods should be validated globally and accepted by a large community of users
Three improvements selected as a first set :
  cloud detection, cloud shadow…
  aerosol content correction
  bidirectional effects correction on syntheses
Development based on :
  proposal of methods to various users and acceptance by IUC,
  training of algorithms on model, real VGT and Polder data sets, presentation and discussion in Belgirate VEGETATION 2000
  extensive validation phase on real data : 10 months, global data processed by CTIV
Actors : VITO & CESBIO

## Slide 4: CLOUD DETECTION
B3 (SPOT4-VEGETATION)
Amazon River, (Venezuela)
Initial mask

## Slide 5: CLOUD DETECTION
BINARY MASK
B3 (SPOT4-VEGETATION)
Amazon River, (Venezuela)

## Slide 6: CLOUD DETECTION
3 LEVEL MASK
B3 (SPOT4-VEGETATION)
Amazon River, (Venezuela)

## Slide 7: CLOUD SHADOW DETECTION
B3 (SPOT4-VEGETATION)
SAHARA.
CLOUDS (light green)
SHADOWS (magenta)

## Slide 8: AEROSOL CORRECTION
Basis for the method : for dark targets, SWIR/Blue surface reflectance ratio was supposed to be constant. Analysis on first years of data, Aeronet stations measurements… showed that ratio was function of surface NDVI Operational algorithm developped as an approximation of a complete iterative solution. Validation of approximation done on VGT, Polder, Aeronet data.
Complete description available in proceedings of VEGETATION 2000

## Slide 9: Principle of the algorithm
_i_toa
SMAC_molecular
If not cloudy and reliable CN
If _swir_surfo<threshold1
&&
NDVI_surfo>threshold2
&& no snow
_i_surfo
blue_reference = _swir_surfo/RATIO
RATIO=AeB.NDVI_surfo
yes
p such as
SMAC_aero(blue_surfo, p) = blue_reference
p_retrieved
SMAC_aerosols
_i_surf
p_climato
no

## Slide 10: Latitudinal transect 20°E

## Slide 11: Latitudinal transect 4°W

## Slide 12: Aerosol Optical Thickness at .550µ (09/11/2001)
0
0.4
0.3
0.2
0.1
0.5

## Slide 13: BI-DIRECTIONAL CORRECTION
COLLECT LAST N CLOUD FREE DATA
AJUST BRDF MODEL
AVERAGE NORMALISED
REFLECTANCES
USING AJUSTED BRDF, NORMALISE CLEAR REFLECTANCES OF LAST TEN DAYS

## Slide 14: DATA SET (2001)
6 MVC10_8km
05/01
05/11
07/01
0711
10/01
10/11
31 NEW BDC SYNTHESES 8KM RES FROM 21/02/2001 TO 31/12/2001
2001
t

## Slide 15: 60 VALIDATION POINTS FOR TEMPORAL PROFILES
Mettre la carte avec la totalité des points

## Slide 16: NDVI (2001) NORTH AMERICA BDC && MVC

## Slide 17: B2 (2001) EUROPE BDC && MVC

## Slide 18: B3 (2001) EUROPE BDC && MVC

## Slide 19: NDVI (2001) EUROPE BDC && MVC

## Slide 20: SWIR (2001) EUROPE BDC && MVC

## Slide 21: B2 (2001) AFRICA BDC && MVC

## Slide 22: B3 (2001) AFRICA BDC && MVC

## Slide 23: NDVI (2001) AFRICA BDC && MVC

## Slide 24: B4 (2001) AFRICA BDC && MVC

## Slide 25: NEW STANDARD PRODUCTS CONCLUSION
Acceptance after long validation phase,
Production began in May 2001 for validation : data are available from that date
Now waiting for next proposals for improvements … but two criteria
  validation
  acceptance by a large community

## Slide 26: VEGETATION 2002
As a follow-on to VEGETATION 2000 in Belgirate, VEGETATION 2002 Nov 19-22, 2002 Antwerp Belgium
Open to presentations of any use of VEGETATION products, either for scientific or more applied purposes
Particular attention to VEGA 2000 and GLC 2000 results
Technical news on quality of the two systems
First announcement in press, look after your (e)mail

## Slide 27: OTHER MEANS FOR EXCHANGE :
Several VEGETATION Web sites with a common entry point : http://www.spot-vegetation.com with several sections : technical, scientific, commercial
Discussion forum available on the entry point : do not hesitate to ask questions, make proposals….

## Slide 28: STATUS OF SPOT VEGETATION
VEGETATION 2
NEW STANDARD PRODUCTS
VEGETATION 2002
Gilbert Saint - VEGETATION Programme Scientist