## Slide 1: GLC-2000 North America: Classification and Results Validation
Chandra Giri
SAIC, EROS Data Center
Zhiliang Zhu
USGS, EROS Data Center
Presented at the GLC 2000 Final Results Workshop Organized by Joint Research Center, Ispra, Italy from 24-26, March 2003

## Slide 2: GLC-2000 NA Classification Methodology
Combined Modified FGDC Classification and LCCS
Unsupervised Classification
Iterative Labeling
Results Validation

## Slide 3: GLC-2000 NA Results Validation
A. Qualitative Assessment
B. Quantitative Assessment
NA window divided into 3 sub-windows
  Canada - Completed
  USA - Completed
  Mexico, CA, Caribbean – On-going

## Slide 4: USA- Reference Data
National Land Cover Data (NLCD)
Landsat ETM+
Forest Cover Types from National Atlas of the United States
7 land cover classes
Equalized random sampling
Minimum 50 sample points per class
Accuracy Assessment

## Slide 5
 | Forest | Shrub | Grass | Wet | Crop | Urban | Water | Total | PA | UA
Forest | 35 | 10 | 1 | 1 | 3 |  |  | 50 | 59.32 | 70.00
Shrub | 5 | 30 | 11 |  | 3 |  |  | 49 | 55.56 | 61.22
Grass | 2 | 8 | 21 | 1 | 15 |  |  | 47 | 55.26 | 44.88
Wet | 1 | 2 | 3 | 28 | 8 | 5 |  | 47 | 84.85 | 59.57
Crop | 2 | 1 | 1 | 1 | 43 | 1 |  | 49 | 55.84 | 87.76
Urban | 11 | 3 | 1 | 1 | 3 | 23 | 2 | 44 | 76.67 | 52.27
Water | 3 |  |  | 1 | 2 | 1 | 43 | 50 | 95.56 | 86.00
Total | 59 | 54 | 38 | 33 | 77 | 30 | 45 | 336 |  | 
Overall Accuracy = 66.37%
Kappa Coefficient = 0.62274
Accuracy Assessment Without Smoothing

## Slide 6
 | Forest | Shrub | Grass | Wet | Crop | Urban | Water | Total | PA | UA
Forest | 37 | 10 | 1 |  | 6 | 1 |  | 55 | 67.27 | 67.27
Shrub | 5 | 35 | 11 |  | 4 |  |  | 55 | 64.81 | 63.64
Grass | 2 | 6 | 20 | 1 | 22 | 1 |  | 52 | 55.56 | 38.46
Wet | 2 |  | 2 | 28 | 6 | 4 |  | 42 | 90.32 | 66.67
Crop | 3 | 1 | 2 | 1 | 47 | 1 | 1 | 56 | 52.81 | 83.93
Urban | 6 | 2 |  |  | 4 | 27 | 2 | 41 | 79.41 | 65.85
Water |  |  |  | 1 |  |  | 42 | 43 | 93.33 | 97.67
Total | 55 | 54 | 36 | 31 | 89 | 34 | 45 | 344 |  | 
Overall Accuracy =68.60%
Kappa Coefficient =0.65635
Accuracy Assessment With Smoothing

## Slide 7: GLC-2000 NA Observations/Experiences
Forest areas better discriminated
GLC-2000
IGBP

## Slide 8
> Inclusion of climate/eco-region information helpful

## Slide 9: GLC-2000 NA Observations/Experiences (Contd.)
Combined FGDC & LCCS Classification System useful
Additional field data/secondary data & VEGETATION data may help improve classification results
Regular communication between CCRS and EDC beneficial

## Slide 10: Poster of North America
Draft