## Slide 1
Vanda Lima
Steering Committee November 2001
I&CLC2000
IMAGE2000 and CORINE Land Cover 2000
a link between the local and global land cover
With contributions from Steve Peedell

## Slide 2
Updating of CORINE Land Cover is
I&CLC2000 Project a Joint EEA-JRC project 3 Years and 10 MEURO Co-funded by DGs REGIO, AGRI, ENV,
JRC; EEA and Member States
IMAGE2000: the spatial reference for Europe,
JRC is responsible for geo-referencing and preparing a multi-purpose mosaic of satellite images (Landsat 7 ETM ), in Co-ordination with the EEA
CLC2000: updating of CORINE Land Cover:
EEA is responsible, in Co-ordination with JRC
CORINE Land Cover- the European Land Cover Data Base
Land Use/Land Cover are affected by every area of policy and economic activity
CORINE Land Cover (CLC) is one of the best tools to inter-link
the Environment with the European policy issues:
Image2000 Web Catalogue

## Slide 3
Basic specifications I&CLC2000
Satellite image spatial reference DB
Landsat 7 ETM+
7 bands + 1 pan (25 m + 12.5 m)
National projection systems
E. Mosaic<1:500 000 ETRS-LCC
E. Mosaic>1:500 000 ETRS-TM
European wide consistent
land cover mapping
Mapping scale 1:100 000
44 standard classes
Minimum mapping unit 25 ha
Update every 10 year

## Slide 4
100 % coverage (EU15)
100 % coverage (AC10)
Stand by (maps missing)
IMAGE2000 ACHIEVEMENTS: CURRENT STATUS

## Slide 5
HIGH DATA ACCURACY:
Technical Specifications RMSE  25 m
Demonstrated High Accuracy through External Quality Control
much better than initially expected:
Average RMSE (x) RMSE (y): (x) 11.26 m and (y) 11.42 and
RMSE (x,y): 16.60 m
Time Consistency :
Acquisition with reference year 2000 (99-01)
IMAGE2000 ACHIEVEMENTS: DATA CONSISTENCY & HIGH ACCURACY
Data Consistency:
In high season: June-September
Centralised Ortho-Rectification (Metria & GISAT)

## Slide 6
Image2000 ACCURACY: TOWARDS ACCURATE SPATIAL REFERENCE
AUSTRIA
X Y
14.59 14.07
(15.88) (16.10)
GERMANY
X Y
12.00 9.00
(19.83) (17.05)
FINLAND
X Y
12.40 11.30
(7.92) (9.91)
NETHERLANDS
X Y
13.30 7.80
(15.28) (7.89 )
IRELAND
X Y
12.70 18.00
(12.20) (18.66)
DENMARK
X Y
10.20 11.40
(14.53) (15.00)
Results from External and Internal Quality Control
Rmse (x), Rmse (y) in meters
SWEDEN
X Y
10.80 10.20
(7.89) (10.03)
UK
X Y
8.90 10.40
(12.45) (14.75)

## Slide 7
IMAGE2000 DATABASE
Use:
Repository, catalogue, dissemination, security
Content:
Individual scenes (Product 1) with
corresponding structured metadata,
ortho-rectified quick-looks,
mosaics (Product 2 and Product 5)
To be implemented:
The integration of Image2000 AC

## Slide 8
A GEOREFERENCED RASTER DATABASE FOR IMAGE 2000
Phase 1
Develop a raster database of the full georeferenced Image 2000 scenes
To assist management of the existing archive
To complement the existing Image 2000 JRC catalogue
To provide the basis for internal project dissemination
Multi-modal access (e.g. via web as a service, via FTP for distribution of original data to selected users, directly as a dataset for analysis internally)
Allow integration with other georeferenced layers
Advantages of a database approach
Controlled, multi-user access
Data management
Data security
Data query
Georeferenced, panchromatic data, 12.5m resolution, extracted from Image2000 database

## Slide 9
Loading the IMAGE2000 database

## Slide 10
Verification: Exemple of Sampling plan for Lot 1, Lot 2 and Lot 4
Working units
Selected verification units
The 10x10 Km grid
Change vector polygons

## Slide 11
I&CLC2000 time frame
June 2002 – IMAGE 2000 ortho-correction completed
End 2002 – first results IMAGE2000 and CLC2000 available for use
Mid 2003 – European mosaic completed (tentative)
End 2003 – project to be completed in order to take full benefits of the results for reporting purposes.