## Slide 1
The Global Burnt Area 2000 initiative: GBA-2000
Mapping, from SPOT-VEGETATION S1 imagery, of the areas burnt globally during the year 2000
J-M. Grégoire
SAI-GVM
22nd March 2001

## Slide 2
The Global Burnt Area 2000 initiative: GBA-2000
A contribution to the Global Land Cover (GLC 2000) initiative
In response to the needs for environmental assessment of the
interactions
between biomass burning and land cover change:
Biodiversity, Desertification and Climate Change Conventions
between biomass burning and emissions of GHG & aerosols:
Climate Change Convention

## Slide 3
    a binary map (burnt-unburnt)
    monthly non-accumulative global burn scar map, at 1 km resolution
    statistics of burnt areas
    area burnt in 2000 per country, per month, and
    per main types of vegetation cover (IGBP-DIS and Hansen et al.)
GBA-2000 Product definition

## Slide 4
GBA-2000 General approach
Selection of a limited number of co-investigators : 8
criteria: access to validation data sets & field expertise/contacts
Development of regional algorithms for processing VGT S1 imagery
to burnt area maps
Integration of the regional algorithms into a global processing chain
at JRC

## Slide 5
GBA 2000 Co-Investigators
CSIRO(AU) - UTL(P) - NRI(UK) - CNR(I) - CCRS (CA) - CRG (CA) - IFI (RU) - SAI (EU)
GBA test-sites (white rectangles; indicative position), with corresponding geographical coordinates (Ul; LR corners)
63N - 81W
44N - 55W
(CRG)
62.5N-112W
57N-104.5W
(CCRS)
18N - 93W
7N - 77W
(NRI)
5S - 75W
20S - 45W
(UTL)
17S - 21E
28S - 29E
(NRI)
10S - 22E
28S - 42E
(UTL)
18N - 18W
0 - 52E
(CNR)
44N - 10W
36N - 0
(UTL)
11S - 125E
21S - 135E
(CSIRO)
60N - 118E
48N - 140E
(IFI)
68N - 45E
60N - 60E
(IFI)
55N - 115E
40N - 135E
(UTL)
10S - 125E
18S - 146E
(GVM)

## Slide 6
GBA-2000 Methodology: Pre-processing
Masking
for clouds & cloud shadows (adapted from Kempeneers et al.,2000)
for extreme viewing zenith angles (> 50o)
for max. NDVI composite areas (+/- 32o Lat.)
for non-burnable areas
. IGBP-DIS (EDC/USGS)
. Simple Biosphere Model 2 (EDC)
. Maryland Global Landcover Dataset (Hansen et al., 2000)

## Slide 7
GBA-2000 Methodology: Processing to burnt area maps
Supervised temporal change detection techniques, on a pixel basis
applied to single date images (NRI, Flasse et al.; UTL, Pereira et al.)
non consecutive images: 5-day cycle (Boschetti et al., 2001)
Supervised temporal change detection techniques, on a pixel basis
applied to composite images (JRC, Stroppiana et al., 2001; IFI, Ershov et al.)
compositing = 10-day, min NIR
Supervised temporal change detection techniques, on a pixel basis but
with a spatial dependency (CNR, Brivio et al.)
applied to single date images
contextual window 3x3
neural network approach
3 approaches currently tested
All based on change detection techniques in NIR, SWIR & NDWI

## Slide 8
GBA-2000 Methodology: Validation
Performance analysis of the algorithm(s)
regression estimator, restricted to the regions covered by high resolution imagery (TM)
+ overall accuracy
+ under and overestimation errors
Validation fo the final map
how to validate a global map of burnt areas ???????
Comparison with other global burnt area product for the year 2000
GLOBSCAR product – from ATSR imagery (ESA/ESRIN)

## Slide 9
GBA-2000 Status on March 2001
Data distribution to co-investigators completed
Development of regional algorithms
+ completed for Australia test-site
+ nearly completed for Africa, Northern hemisphere
Africa, Namibia/Botswana site
+ initiated for Africa, Mozambic test-site
Russia, Far East Siberia
Canada
+ evaluation during the GOFC-Fire workshop, Lisbon, July 9-11
Global processing chain at JRC
+ pre-processing module completed
+ processing module: tests started over the African continent