## Slide 1
Problems encountered using Along Track Scanning Radiometer data for continental mapping over South America
Requirement for updating the forest extent maps created under the TREES I project (1992 AVHRR 1 km data)
Possibility of using a ‘new’ European sensor ATSR on the ERS-2
VNIR / SWIR / MIR / TIR / 1 km resolution / geometrically corrected / NRT or Central service / Two looks / 500 km swath / 10AM-10PM
Due to the large area to be covered and the small swath (and clouds) mosaicing was required

## Slide 2
SWIR/NIR/RED (RGB) ATSR-2 over Rio Branco
50 km

## Slide 7
West of image – satellite ‘views’ illuminated canopy
East of image – satellite ‘views’ into the shaded canopy
Satellite
Sun

## Slide 8
Within image spectral confusion (e.g. dense forest on west of image / degraded forest on east of image)
Biased pixel selection and spectral confusion in mosaics
Solutions?
Throw away half of each image (! We would never have enough data)
corrections based on known BRDF models of landcover (need to know the cover type)
construct the models for our database and then invert (atmospheric contamination of haze effects the data base)

## Slide 9
In practice
– used the RPV (Rahman et al. 1993) –
Empirical coefficients are used along with the Sun-Target-Sensor geometry to correct the data.
p corrected = p(v,u,φ,j, k, H)
v,u,φ – are viewing geometry angles
J,k,H are optimised coefficient

## Slide 13
Problems
unable to adequately establish stable parameters for the RPV polynomial (atmospheric contamination?)
the available time series was too erratic – not enough images in certain areas and in certain seasons
Mosaics were produced –
Highest Tsurface (“tropical dry season”) (clean images but highly contrasted)
Highest NDVI (“tropical wet season”) (pixelated)
- Lowest SWIR (“moist / shadowed”) (cloud shadow and haze)

## Slide 14
Lowest SWIR
Highest Tsurface

## Slide 16
Ts
NDVI
SWIR
Input images
Output mosaics
Mosaicing used as a means of selecting the best images for particular seasons
smaller mosaics then constructed for ecological regions

## Slide 17
Lessons for VGT data
the same problem exists
the exceptional data availability means that compositing should be more feasible

## Slide 18
Need for:
BRDF corrected images – if possible independent of existing land cover classification
Mosaicing techniques that reflect vegetation in different states – “dry” and “wet” season images and avoid the following problems
  Cloud shadow
  Haze
  Smoke
  “Pixelation”