## Slide 1: WP 1 : Improvements of products and services
Cloud and cloud shadow detection : VITO Atmospheric correction : CESBIO Bidirectional effects correction : CESBIO
All material extracted from presentations in Belgirate
G. Saint, CNES

## Slide 2: CLOUD AND SHADOW DETECTION
OPERATIONAL CONSTRAINTS FOR THE ALGORITHM.
Must work in near real time : SPEED (simplicity) REQUIRED.
Must be ACCEPTABLE to the user community.
Must work on the VEGETATION instrument (no TIR bands).
Must be GLOBAL and CONSISTENT
Must have three levels CLOUD-UNCERTAIN-CLEAR

## Slide 3: CLOUD AND SHADOW DETECTION
CRITERIA FOR CLOUD DETECTION
A pixel is declared cloudy if all spectral bands have higher values than the corresponding thresholds.
Only two thresholds are ‘binding’ : B0 and SWIR
OPTIMISATION ENGINE
Specially developed dedicated Genetic Algorithm
RESULTS
Binary cloud mask (threshold on B0 and SWIR)

## Slide 4: CLOUD AND SHADOW DETECTION
THREE LEVEL CLOUD MASK
Apply binary mask to a large number of images
Make histograms of clear and cloudy pixels over all regions
Select a region of uncertainty around the thresholds
Label the corresponding values as the lower and upper thresholds
Resulting protocol for cloud detection:
A pixel is labeled CLEAR if : B0<493 OR SWIR<180
A pixel is labeled CLOUDY if : B0>720 AND SWIR>320
A pixel is labeled UNCERTAIN in all other cases.
(Thresholds are digital numbers of the VGT-P products)

## Slide 5: CLOUD AND SHADOW DETECTION
Validation:
Cloud detection was validated by means of comparison to synoptic observations of cloud cover in stations over the world (data set courtesy of Météo-France)
Performance was satisfactory (average error of cloud cover < 14%), especially considering all the differences between synoptic observations and satellite observations (measurement scale, FOV, time differences, mountains, subjectivity of human observer,…)

## Slide 6: CLOUD AND SHADOW DETECTION
SHADOW DETECTION : GEOMETRIC MODEL
N
h
shadow
cloud
r
v
av
s
R
sun
sat
p

as


## Slide 7: CLOUD AND SHADOW DETECTION
Example
B3 channel of SPOT4-VEGETATION image of the Sahara desert, Algeria.
cloud mask (light) and shadow mask (dark) calculated with the specified algorithms

## Slide 8: CLOUD AND SHADOW DETECTION
Evolution of the cloud mask (1)
B3 channel of SPOT4-VEGETATION image of the Amazon, Venezuela
First Binary Cloud Mask (Before start of the project)

## Slide 9: CLOUD AND SHADOW DETECTION
Binary cloud mask (implemented now)
B3 channel of SPOT4-VEGETATION image of the Amazon, Venezuela
Evolution of the cloud mask (2)

## Slide 10: CLOUD AND SHADOW DETECTION
Three Level Cloud Mask (Future)
B3 channel of SPOT4-VEGETATION image of the Amazon, Venezuela
Evolution of the cloud mask (3)

## Slide 11
WP1.1.2 Improvement of atmospheric corrections through a better evaluation of the aerosol content

## Slide 12: A Simple Method for Atmospheric Correction SMAC (Rahman and Dedieu, 1994)
toa= tg *[ a ()+ T(s,)*T(v,)*s ( , )/(1 - s(, )*s)]
  H2O outputs of a meteorological Model (ARPEGE)
  O3 Climatology (TOMS)
  p latitudinal climatology
One equation by channel
Two unknowns by equation :  and s
SOLUTION : interspectral relationship :
SWIR/BLUE RATIO at the surface

## Slide 13: ‘ Actual ’ SWIR/Blue values using AERONET AOTs measurements
15 test sites
(various biomes)

## Slide 14: The ‘ Actual ’ SWIR/Blue relationship
The ratio looks NDVI dependent over green targets
TOA NDVI

## Slide 15: The iterative method
RATIO=1
For NB_ITER=1 to NB_ITER=NB_ITERMAX
  RATIO=0
  For date=1 to date = NBDATES
    FIND p_MIN such as [blue_surf(p) - RATIO*swir_surf(p)] is minimum
    blue_surf=SMAC(blue_toa)
    swir_surf=SMAC(swir_toa)
    ratio(date)= swir_surf/ blue_surf
    RATIO+=ratio(date)
  RATIO=RATIO / NBDATES
Assumes a constant ratio during a time period (NBDATE)
Finds the AOT time profile to fit the MEAN RATIO to the assumption
Re-iterates with the new ratio value
Convergent (monotonic and bounded correction of blue reflectances)

## Slide 16: The iterative retrieval of the SWIR/BLUE ratio
An efficient method but computationally too expensive
 not suitable to be implemented in the VEGETATION production line.
Can be used as reference in order to calibrate another approach

## Slide 17: Histogram analysis on the ratio distribution versus TOA NDVI

## Slide 18: Comparison of AOT retrievals ratio(NDVI) AND ratio_iter
RATIO(NDVI)
RATIO_iter

## Slide 19: Comparison between SURFACE reflectances
CLIMATOLOGY
ITERATIVE
ratio(NDVI)
RED CHANNEL

## Slide 20: CONCLUSIONS
THE SWIR/BLUE RELATIONSHIP AT THE SURFACE IS TIME AND LOCATION DEPENDENT: Greeness = Prime driver
AN EFFICIENT AND ORIGINAL ITERATIVE METHOD WAS USED AS REFERENCE TO CALIBRATE A SIMPLE RELATIONSHIP BETWEEN SWIR/BLUE (surface) AND NDVI (TOA)
THE RESULTING METHOD IS NOT EFFICIENT ON ARID TARGETS (Bright reflectances) WHERE THE CLIMATOLOGY SHOULD BE KEPT
OTHER CASES SHOW LARGE IMPROVEMENTS WITH REGARD TO THE CURRENT CLIMATOLOGY (semi-transparent clouds are processed)

## Slide 21
WP1.1.3 Introduction of directional model in compositing technique

## Slide 22: NORMALISATION OF BIDIRECTIONAL EFFECTS
Normalisation = correction of Top of Canopy (TOC) reflectance (s, v, ) along the shape of the Bidirectional Reflectance Distribution Function (BRDF) to a reference geometry (s0, v0) :
NORM = OBS  MOD(s0, v0) / MOD(s, v, )
( Gutman 1995 / Wu et al. 1995 )
BRDF model of Roujean et al. (1992) :
MOD(s, v, ) = k0 + k1 f1 (s, v, ) + k2 f2 (s, v, )
Common approach : three-step process
  1. collect the data along a sliding time window of constant length
  2. fit a BRDF model 3. normalise & compose a subset of data.

## Slide 23: SIMULATION OF VEGETATION DATA
VEGETATION Acquisition Geometry
Cloud Cover Temporal Evolution
Top of Canopy Reflectance from the BRDF POLDER Data Base ( Bicheron et al. 2000 )
‘Gaussian’ Atmospheric Noise
  DATA BASE OF TOP OF CANOPY (TOC) REFLECTANCES TIME SERIES

## Slide 24: TESTING COMPOSITING METHODS USING SIMULATED DATA (1)
  MVC = maximum NDVI ( Holben 1986 )
  BRDF-MVC = MVC normalised  corrected along the BRDF shape to (s0, v0) geometry
  BRDF-10 = Average of last 10-days cloud-free reflectances after normalisation in (s0, v0)
  2 & 3 with BRDF is retrieved on 30-days time window
  Simulation  Reference level :  (  v0 ,  s0 )
   s0 = mean (  s ) ;  v0= 0°
Day of Year
TOC red reflectance

## Slide 25: TESTING COMPOSITING METHODS USING SIMULATED DATA (2)
  Noise  ( 1 / 2 / 3 ) -  ( v0 ,  s0 )
  MVC selects particular views
  Noise is maximum, non-consistent with cloud coverage (and depends on BRDF shape)
  BRDF-10 & -MVC comparison :
  Averaging is better than choosing one particular data
  Noise is minimum for BRDF-10 and input atmospheric noise is reduced by a factor 2
NOISE on 10-days reflectance

## Slide 26: NEW ALGORITHM BDC : Bi-Directional Compositing
MAIN IDEA : COLLECT A CONSTANT NUMBER OF DATA TO FIT THE BRDF, REGARDLESS TO THE DATE OF ACQUISITION
BRDF shapes supposed - and believed - to slowly vary (on cloudy areas)
But reflectance levels vary at a 10-days step, due to compositing method
COLLECT THE N (12) LAST CLOUD-FREE DATA
FIT THE BRDF MODEL
USE BRDF-10 TO NORMALISE AND COMPOSE DATA

## Slide 27: RESULTS ON VEGETATION IMAGES
MVC Europe - 10/09/98 BDC
MVC selects off-nadir views in forward scattering
MVC is low contrasting
BDC reflectances are higher than MVC
BDC is better cloud-filtered
snow is not detected

## Slide 28
 BDC removes orbital tracks
(NDVI)and bidi-rectional artefacts(NIR)
MVC Zambia - 30/04/98 BDC
RESULTS ON VEGETATION IMAGES

## Slide 29: RESULTS ON TIME SERIES (RED & NIR)
BDC time series are smoother than MVC, due to nadir-like viewing
MVC is in red, BDC in blue
MVC is in red, BDC in blue

## Slide 30: RESULTS ON TIME SERIES (NDVI)

more quantitative method for analysing ‘high frequency time fluctuations’ ( Leroy et al. 1999 ) :

MVC is in red, BDC in blue

## Slide 31: CONCLUSION
MAIN OUTCOMES FROM SIMULATION :
Proves the limitations of MVC,
Quantifies the improvements of bidirectional normalisation and averaging of data
Shows that the common concept of sliding time window is not operational
NEW CONCEPT : COLLECT A FIXED DATA SET TO RETRIEVE THE BRDF
BDC is self-consistent (no external information is required),
homogeneous (no alternative method is used),
pertinent to qualify of data (cloud-filtering, statistics on the fit of BRDF)
FIRST RESULTS FROM ACTUAL VEGETATION DATA :
High contrasting and smoothness (for all spectral bands & NDVI)
To be calibrated and validated at broad scales in space and time